## Slide 1: Function Generator
Team : S Nitro S
EN-2091 Laboratory Practice and Projects – Analog Project

## Slide 2
Introduction
What is our implementation ?
This implementation is done by using op-amps, resistors, transistors, capacitors and
potentiometers.
 Functions :-
Sine Wave
Triangular Wave
Saw-tooth Wave
Square Wave
PWM Wave ( duty cycle vary from 1% up to 99%)
 Capabilities :-
Adjustable amplitude (From 0 V to 10 V)
Adjustable frequency (from 20 Hz to 20 kHz)
DC shift

## Slide 3
Block Diagram
Sine Wave
Triangular Wave
Saw – tooth Wave
Square Wave
Frequency Changer
Frequency Changer
PWM Wave
DC Shift
Amplifier Circuit
Output Circuit

## Slide 4
 Square Wave
Square wave is generating using a Relaxation oscillator circuit
The frequency of the square wave can be changed by varying the values of the potentiometers.
Components
Op-Amp - AD711JN
Slew rate – 16V/us , Unity gain bandwidth – 3MHz
power supply (3V -18V)
Potentiometers – 10 kilo ohm, 250 kilo ohm
Resistors – 100 ohm, 1 kilo ohm, 10 kilo ohm
Capacitors - 1uF , 0.1uF , 0.01uF
Waveform Generation

## Slide 5
 Triangular Wave
Components
The triangular is generated using a cascade combination of a Schmitt trigger circuit and an integrator.
By changing the value of the resistor R1, we can change the frequency of this oscillation.
Op-Amp - AD711JN
Slew rate – 16V/us , Unity gain bandwidth – 3MHz
power supply (3V -18V)

## Slide 6
 PWM Wave
Components
Generation of PWM wave can be done by comparing the triangular wave with a DC level.
The duty cycle of the PWM signal can be varied by changing the Resistance value.
Frequency of the PWM wave can be changed by changing the frequency of the triangular wave.
Op-Amp - AD711JN
Slew rate – 16V/us , Unity gain bandwidth – 3MHz
power supply (3V -18V)

## Slide 7
 Sine Wave
Wien bridge oscillator circuit is used to generate the sine wave.
The circuit generates a sine wave at the resonance frequency(fr),
fr =
The frequency of the sine wave can be changed by varying the values of the two resistors or the two capacitors simultaneously.
Components
Op-Amp - TL071CP Slew rate – 16V/us , input bias current – 5pA
power supply (3V -18V)
10 kilo ohm potentiometers – 2
Capacitors - 1 k , 10 nF , 100 nF , 1 uF , 10 uF

## Slide 8
 Saw-tooth Wave
Components
To generate saw-tooth waveform we connect the non-inverting terminal of the integrator to a DC voltage value.
We use the potentiometer to adjust the DC voltage.
Op-Amp - TL072CP Slew rate – 20V/us , Low noise: Vn = 18 nV/√Hz
power supply (3V -18V)
2N3904 Transistor
100 kilo ohm potentiometers and 10 kilo ohm resistors

## Slide 9
 Amplifying Circuit & DC shift
 Output Circuit within Buffer
We provide a DC shift by using a summing amplifier circuit to the inverting amplifier op-amp
Same op-amp is used to change the gain of the signals
We use a buffer circuit to isolate the output circuit and the function generator circuits while obtain a unity gain.
We use a push pull amplifier output circuit to drive a low resistance load and to amplify the current and power.

## Slide 10
Frequency Ranges
Capacitor | 250Kohm Potentiometer | 10Kohm Potentiometer
0.01uF | 12KHz – 542Hz | 41KHz – 12.5KHz
0.1uF | 1.8KHz -73Hz | -
1uF | 140Hz – 11Hz | -
Capacitor Value | Frequency Range
10uF | 20 Hz – 130 Hz
1uF | 100 Hz – 550 Hz
100nF | 500 Hz – 4.5 kHz
10nF | 4 kHz – 15 kHz
1nF | 14 kHz – 20 kHz
 Sine Wave
 Square, Triangular, PWM & Saw-tooth

## Slide 11
Multisim Schematic Diagram

## Slide 12
PCB Schematic Design

## Slide 13
PCB Design

## Slide 14: PCB

## Slide 15
Enclosure

## Slide 16
Testing & Debugging

## Slide 21
Bill of Quantities
Component | Quantity | Price Rs/=
AD711LN IC | 3 | 6300
Ad712JNZ | 1 | 2200
TL072CP IC | 3 | 270
Potentiometers | 7 | 2460
Switches | 7 | 720
TIP31c | 2 | 30
TIP32c | 2 | 24
2N3904 | 1 | 6
Capacitors, resistors, diodes and JST wires |  | 1500
3D Printing | - | 5200
PCB Design Cost | - | 3900
TOTAL |  | 22 610/=

## Slide 22
Team Members & Task Allocation
ALAHAKOON U.M.Y.B. 210027C
Square, Trangular wave Generating Circuit and Altium Designing
DULNATH W.H.R. 210152E
Wein bridge oscillator Circuit, Circuit Simulations and Altium Designing
HANSINDU K.A.A. 210204R
PWM, Saw-Tooth Wave generator Circuit Testing
SHAMIKA K.A.M. 210600D
Amplifier, Output circuit and Enclosure designing

## Slide 23
Thank You